Фамилия, инициалы:________________________________________________

Reference class sub-bass system designed for use with the very finest stereo and multi-channel audio systems in larger rooms.

- True 500W (continuous) discrete, direct-coupled MOSFET amplifier

- 2x downward-firing long-throw 250mm (10”) very heavy duty “Volt” drivers, die-cast chassis

- Refined ABC® variable crossover adjustment in 24 musically correct semi-tone increments between 24Hz-106Hz.

- Acoustic Resistive Matrix (ARM) loading for smoother bass response

- Four position mode selector: line/LFE (0 degrees phase and 180 degrees phase)

- Audiophile grade toroidal transformer

- Gas-tight Neutrik high level connection for long-term consistency of sound quality

- High quality, panel-mounted twin phono inputs at 0dB and +12dB (low level)

- High and low level balanced inputs (Neutrik/XLR)

- Totally discrete input circuitry for high and low level inputs

- Separate volume controls for high and low-level adjustment

- Simultaneous connection of high and low level sources

- Set-Safe® audibly transparent driver protection

- Balanced-bridge power supply

- 8x ultra-rugged output devices

- Double thickness, double-sided glass-fibre board with plated-through holes

- IEC power input socket - no captive leads for installation flexibility

- Hand-built in Great Britain, three year worldwide warranty

| Specifications |  |
| --- | --- |
| System Type | ARM loaded cabinet with ABC® semi-tone variable bass filter. 110 litre. |
| Lower Frequency Response | (in room -6dB): 9Hz |
| Amplifier Input impedance | High level 100 kOhm |
| Gain Control Range | Low level 10 kOhm 80dB |
| Drive unit impedance | 8 Ohm |
| Mains input voltage | 115 V 50/60 Hz or 230 V 50/60 Hz, subject to country |
| Finishes | Black Oak, Cherry, Light Oak, Rosenut, Walnut ( subject to country of sale) |