| Aircraft | An-3T | Cessna 208A (Caravan 1) | Cessna 208B (Grand Caravan) |
| --- | --- | --- | --- |
| Dimensions |
| Length, m | 13,965 | 11,5 | 12,6 |
| Height, m | 4,93 | 4,5 | 4,5 |
| Upper wing span, m | 18,176 | 15,9 | 15,9 |
| Wing area, м2 | 71,5 | 26 | 26 |
| Cargo cabin |
| Lenght, m | 4,21 | 3,8 | 5,1 |
| Width, m | 1,65 | 1,58 | 1,58 |
| Volume, м3 | 12 | 7,2 | 9,8 |
| Underfuselage space volume, м3 | none | 2,4 | 3,2 |
| Take-off weight, kg | 5800 | 3632 | 3969 |
| Payload max, kg | 1800 | 1400 | 1600 |
| Passengers | 9 according to AP23,12max | 9 according to FAR23,13max | 9 according to FAR23,13max |
| Engine |
| Type | TVD-20 | РТ6А-114 | РТ6А-114А |
| Power, hp | 1375 | 610 | 685 |
| Empty weight, kg | 3615 | 2016 | 2149 |
| Fuel max, kg (у=0,775) | 1271 | 1020 | 1020 |
| Cruising speed, km/h max for max distance | 235 235 | 345 289 | 337 287 |
| Cruising height, m max while transporting passengers | 3900 2000-3000 | 7800 up to 3000 | 7200 up to 3000 |
| Range ability, km |
| With 1800 kg | 250 | - | - |
| with 1600 kg | 450 | - | 350 |
| with 1400 kg | 650 | 350 | 750 |
| with 1200 kg | 900 | 800 | 1160 |
| Take-off and landing characteristics |
| Take-off run, m | 140 | 367 | 416 |
| Path length, m | 95-105 | 227 | 290 |
| Runway length required (ISA, SL) | Less than 500 | 674 | 738 |
| Crew | 2 | 1 | 1 |

# Footnotes

If operated without oxygen equipment