SIPAC S.p.A. - Sede operativa ed amministrativa: Via Berettinazza n. 25 - 43010

Fontevivo (PR) – Italia Tel. +39 0521 611811 r.a.  - Fax +39 0521 611850  -

E-MAIL: sipac@sipac.pr.it - Website: www.sipac.pr.it

Sede legale: Strada Giuseppe Garibaldi n. 22 – 43100 Parma  - Italia

Codice Fiscale e P.IVA:  01646860344

CAMERA SORTER

Table of contents

- Camera Sorter Layout _________________________________________________Page 3-4

- Description of how the Camera Sorter works _______________________________Page 5

- Description of how the Vision System works  _______________________________Page 6-8

- Camera Sorter Data Sheet  _____________________________________________Page 9

  - Leuze PRK18B.T2/4P-M12 Photocell  (cod. 14-03-006-030-2) ______________ Page 9-12

  - Telestar IE-58 ZB36 4096 LD5V K1/2/0+N ALB.10FL 12P 40410364 Encoder __Page 13-15

  - 440G Guard Master Locking Switches Allen Brandley TLS-Z_________________Page 16

- Manual installation Annex - Version 8_____________________________________Page 17-35

- Annex Operator Manual ENG.

- Schema Elettrico Selezionatore a Telecamera.

- Distinta Elettrica materiale EL SIPAC.

- Camera Sorter layout

KEY:

M130( BRUSHLESS MOTOR FOR FINGER ROTATION

M131( BRUSHLESS MOTOR FOR FINGER OPENING-CLOSING

M132( ASYNCHRONOUS 3-PHASE MOTOR FOR SPACER

M133( ASYNCHRONOUS 3-PHASE MOTOR FOR SPACER

701B1( Trigger Photocell  Leuze PRK18B.T2/4P-M12

701B2( Fallen bottle Safety photocell Leuze PRK18B.T2/4P-M12

701B3( Fallen bottle Safety photocell Leuze PRK18B.T2/4P-M12

701B4( Fallen bottle Safety photocell Leuze PRK18B.T2/4P-M12

701B5( Fallen bottle Safety photocell Leuze PRK18B.T2/4P-M12

701B6( Stuck bottle Safety Photocell Leuze PRK18B.T2/4P-M12

701B7( Stuck bottle Safety Photocell PRK18B.T2/4P-M12

707S1( Perimetral door with electric lock 440G Guard Master Locking Switches Allen Brandley TLS-Z

707S2( Perimetral door with electric lock 440G Guard Master Locking Switches Allen Brandley TLS-Z

707S4( Perimetral door with electric lock 440G Guard Master Locking Switches Allen Brandley TLS-Z

707S6( Perimetral door with electric lock 440G Guard Master Locking Switches Allen Brandley TLS-Z

708S1( Perimetral door with electric lock 440G Guard Master Locking Switches Allen Brandley TLS-Z

708S4( Perimetral door with electric lock 440G Guard Master Locking Switches Allen Brandley TLS-Z

130B7( Telestar Encoder IE-58 ZB36 4096 LD5V K1/2/0+N ALB.10FL 12P 40410364

CAMERA AND LIGHTING SPECIFICATIONS

KEY:

48HL1( LINEAR BAR LIGHTING WITH WHITE LIGHT LED L420MM ELECTRON. GENESIS COD. GEM42-6K-T

48HL3( LINEAR BAR LIGHTING WITH WHITE LIGHT LED L420MM ELECTRON. GENESIS COD. GEM42-6K-T

48HL5( LINEAR BAR LIGHTING WITH WHITE LIGHT LED L420MM ELECTRON. GENESIS COD. GEM42-6K-T

48HL7( LINEAR BAR LIGHTING WITH WHITE LIGHT LED L420MM ELECTRON. GENESIS COD. GEM42-6K-T

150E1( CAMERA SERIES INSIGHT 7000 12mm COGNEX COD. IS 7010-01-420-000 FROM THE TOP

151E1( CAMERA SERIES INSIGHT 7000 12mm COGNEX COD. IS 7010-01-420-000 FROM ONE SIDE

151E2( CAMERA SERIES INSIGHT 7000 12mm COGNEX COD. IS 7010-01-420-000 FROM ONE SIDE (Optional)

152E1( CAMERA SERIES INSIGHT 7000 12mm COGNEX COD. IS 7010-01-420-000 FROM BELOW (Optional)

- Description of how the camera sorter works

The bottles flow on the conveyor till they reach the spacer, which creates spaces among the bottles.

Subsequently, the bottles enter the bottle sorter. The bottle sorter, depending on its detection, communicates with the divider, which then selects the adequate distribution channel.

The photocell 701B1 is used like a “Trigger” (count).

The photocells 701B2-701B3-701B4-701B5 are used like safety devices for fallen bottles and, in case they are operated, they stop the machine according to the set up filter.

The photocells 701B6-701B7 act as safety devices against the channel obstruction.

The micro 701B8 has two functions:

1. Verify the finger position (if retracted).

2. Verify the safety of the pin, in other words, if the pin is in the correct position to avoid any damage.

In order to determine the bottle position and the synchrony between the finger speed and the conveyor, one encoder(103B7) is installed on the motor bearing downstream the sorter.

The camera sorter is equipped with 7 micro safety doors Schmersal (701S1-S2-S4-S6, 708S1-S2-S4); once the contact is open in working position, the micros immediately stop the sorter.

The motors M130-M131 are Brushless and Lexium-operated.

The motor M130 determines the fingers rotation. The fingers rotate in coordination and in synchrony with the conveyor, while for the motor M131 the pin is raised or lowered.

Finally, the motors M132-M133 determine the rotation of the spacer’s rollers.

- Description of how the vision systme works

CAMERA AND LIGHTING SPECIFICATIONS

The vision system’s task is to identify the bottle type and classify it depending on SHAPE, SIZE and INSCRIPTION.

The a.m. vision system can be used to determine:

- Bottle with a different shape( With lateral camera or upper vertical camera (basement).

- Bottle with a different height( With lateral camera only if the difference between the minimum/maximum tolerance is bigger than 2 mm and there is no overlapping in the tolerance measures of the 2 bottles.

- Bottle with a different diameter( With upper vertical camera (basement) only if the difference between the minimum/maximum tolerance is bigger than 2 mm and there is no overlapping in the tolerance measures of the 2 bottles.

- Bottles with medallions and bottles without medallions( If the medallions of the cylindrical bottles are positioned on the bottle shoulder where the upper vertical camera can detect them (basement). In any case feasibility to be confirmed with trials on samples.

- Bottles with medallions and bottles without medallions ( With one lateral camera for non-cylindrical bottles oriented and which can rotate during their trip.  In any case feasibility and performance to be confirmed with trials on samples.

- Bottles with medallions and bottles with 2 medallions ( If the medallions on the cylindrical bottles are positioned on the shoulder and can be detected by the upper vertical camera (basement). In any case feasibility to be confirmed with trials on samples.

- Bottles with medallions and bottles with engravings ( If the medallions on the cylindrical bottles are positioned on the shoulder and can be detected by the upper vertical camera (basement) and verifying that:

a) The medallions dimensions are different from the engravings.

b) If the difference between the minimum/maximum tolerances is bigger than 2 mm and the tolerance dimensions do not overlap. In any case feasibility and performance to be confirmed with trials on samples.

- Bottles with medallions and bottles with engravings ( With lateral cameras on non-cylindrical oriented bottles, which do not rotate during their trip.

In any case feasibility and performance to be confirmed with trials on samples.

- Bottles with lateral bottom notch with bottles without (In the cylindrical bottels, if shadows are in a visible area and can therefore be detected by the upper vertical camera (basement).

In any case feasibility and performance to be confirmed with trials on samples.

- Bottles with different lateral bottom notch (NO.

Workstation 1-2-3:

For these two applications, the standard Cognex camera is provided, controlled by one PatMax algorithm, in order to have more instruments available in case of need.

Workstation 4:

For these two applications, the standard Cognex camera is provided, controlled by one PatMax algorithm, in order to have the highest possible reliability.

As an option, a 15” Touch Screen color operator console series Advatech 15.6 can be installed (other consoles by other brands can also be used, as long as they are provided with the software to control the Cognex cameras).

The console shall be installed in front of the Electrical panel board on a push-button console close to the cameras and shall be used to visualize the camera images, to interact and access to partial adjustments and calibration of the vision system.

The camera lighting are necessary to illuminate the detection areas and are indicated by the acronyms 48HL1-48HL3-48HL5-48HL7.

4. Camera Sorter Data Sheet

4.1 Photocell  Leuze PRK18B.T2/4P-M12 (cod. 14-03-006-030-2)

4.2 Encoder Telestar IE-58 ZB36 4096 LD5V K1/2/0+N ALB.10FL 12P 40410364

4.3 440G Guard Master Locking Switches Allen Brandley TLS-Z

Below one link with the indications for installation, electrical specifications and all the necesary pieces of information for wiring and installation of the electric lock. http://literature.rockwellautomation.com/idc/groups/literature/documents/in/440g-in007_-en-p.pdf

The installation of GUARD MASTER is optional; therefore, it is not included in the camera sorter’s main offer.

6. Annex manual version 8 istallation